## Slide 1
MICROP
Natalia Cedeno & Ian Green
April 26, 2022

## Slide 2: Optical vs RF
https://www.japcc.org/electronic-warfare-the-forgotten-discipline/
Notes: IAN (natalia answers some qn)
RF domain crowded and contested

## Slide 3: Motivation
Notes: Natalia

## Slide 4: Solution
UAV mounted FSOC
Electro-optical transceiver
  Small form-factor pluggable (SFP) module
Near IR (850nm)
DJ Scanning Galvanometer
Notes: NATALIA

## Slide 5: Work Breakdown Structure
System Description
Notes: NATALIA

## Slide 6: Dynamic System Diagram
Physical Diagram
Media Converter
SFP
Ethernet
Collimator
Lens
Scanner
RPi
Aiming Laser
Camera
DAC
Op Amp
DRIVER
COMMS
Notes: NATALIA

## Slide 7: Dynamic System Diagram
Software Diagram
Position
Observer Log
Camera Analyzer
Logger
Estimator
Scanner
Driver
Camera
Motor
Notes: IAN

## Slide 8: Working Setup
Notes: IAN

## Slide 9: Overcoming Obstacles
Creative Problem Solving
Delivery issues
  More work
ILDA Controller
  Custom driver
Integration of software
  Cry in C++
Notes: NATALIA

## Slide 10
Data Analysis

## Slide 11: Attenuation Testing
Wire | No Collimator (µW) | 780 nm Collimator (µW)
LC-LC | 344.5 | N/A
LC-UPC | 320.5 | 302.6
LC-APC | 80.2 | 73.0
Notes: Natalia

## Slide 12: Camera Integration
Average Green: 239
Average Green: 37

## Slide 13: Software Testbed
VM2
VM1
VM1
VM1
VM2
VM2
Unidirectional
Bidirectional
Parallel
Notes: Ian

## Slide 14: Software Testbed
VM2
VM1
VM1
VM1
VM2
VM2
Fiber
FSOC
Ethernet
MC
MC
MC
MC
Notes: Ian

## Slide 15: Throughput Testing
Notes: Ian

## Slide 16: Throughput Testing (cont.)
Notes: Ian

## Slide 17: Throughput Testing (cont.)
Setup | Bidirectional | Parallel | Unidirectional
Experimental | 930 ± 106 | 889 ± 83 | 941 ± 23
Ethernet Control | 926 ± 118 | 863 ± 112 | 941 ± 23
FSOC | 941 ± 192 | 871 ± 259 | 941 ± 192
One Port Control | 2896 ± 326 | 1631 ± 269 | 2912 ± 415
Shared Host Port Control | 2730 ± 25 | 1575 ± 100 | 2726 ± 23
Notes: Ian

## Slide 18: Latency Testing
Notes: NATALIA

## Slide 19: Latency Testing (cont.)
Setup | Latency (ms)
Fiber | 1.44 ± 0.36
FSOC | 1.66 ± 0.30
Ethernet Control | 1.32 ± 0.22
One Port Control | 1.06 ± 0.26
Shared Host Port Control | 1.1 ± 0.33
Notes: NATALIA

## Slide 20: Bit Error per Gb
Notes: Ian

## Slide 21: Bit Error per Gb (cont.)
Notes: Ian

## Slide 22: Bit Error per Gb (cont.)
Setup | Bidirectional | Parallel | Unidirectional
Fiber | 61 | 230 | 73
FSOC | 102 | 295 | 121
Ethernet Control | 108 | 246 | 73
One Port Control | 5385 | 2777 | 5340
Shared Host Port Control | 5532 | 2546 | 5487
Notes: Ian

## Slide 23
Conclusion

## Slide 24: Future Years
Expanding the Testbed
Dual-dynamic testing
  Second scanner
Outdoors testing
  Increase distance
  Eye-safety
Automated parameter sweep
Photo Credit: Alek Yegazarian
Notes: IAN

## Slide 25: More Info
Longer Demo Video
Poster

## Slide 26
Questions?

## Slide 27
Backup Slides

## Slide 28
Onboarding

## Slide 29: Onboarding - Hardware
Familiarize yourself with Koruza: https://github.com/IRNAS/KORUZA
Read DAC0830/DAC0832 datasheet
Read up on Raspberry Pi GPIO pins: https://projects.raspberrypi.org/en/projects/physical-computing/1#:~:text=GPIO%20stands%20for%20General%2DPurpose,on%20or%20off%20(output)
Understand op-amps: https://www.electronics-tutorials.ws/opamp/opamp_1.html
Understand galvanometer: https://nationalmaglab.org/education/magnet-academy/watch-play/interactive/galvanometer#:~:text=A%20galvanometer%20is%20an%20instrument,can%20deflect%20a%20magnetized%20needle.

## Slide 30: Onboarding - Optics
Read up on basics of FSOC: https://en.wikipedia.org/wiki/Free-space_optical_communication
LC/APC/UPC: https://www.thefoa.org/tech/connID.htm
Terminology: https://blog.router-switch.com/2019/08/optical-communication-terminology-cheat-sheet/
Review lenses and optical physics: https://www.physicsclassroom.com/class/refrn/Lesson-5/The-Anatomy-of-a-Lens#:~:text=A%20lens%20is%20merely%20a,to%20produce%20their%20own%20image.

## Slide 31: Onboarding - Software
Learn C++ Style: https://google.github.io/styleguide/cppguide.html
Learn modern C++: https://docs.microsoft.com/en-us/cpp/cpp/welcome-back-to-cpp-modern-cpp?view=msvc-170#:~:text=Modern%20C%2B%2B%20emphasizes%20the%20principle,deletes%20it%20in%20its%20destructor.

## Slide 32
Install Guide

## Slide 33: Installing – Software
Download software from the GitHub onto Raspberry Pi:
  https://github.com/LMU-Capstone/microp
`cd` into the directory `software/MICROP`
Run `g++ main.cp src/*.cpp -I./include -pthread –lwiringPi -o microp.o`
You can now run using `./microp.o`
Done!
Note: Requires Raspberry Pi 3 or newer with C++11 or above.

## Slide 34: Installing – Demo Software
Download software from the GitHub onto Raspberry Pi:
  https://github.com/LMU-Capstone/microp
`cd` into the `software/demo` folder
Run `g++ LMU.cpp src/*.cpp -I./include -pthread –lwiringPi -o microp.o`
Now run `./microp.o`
Note: Requires Raspberry Pi 3 or newer with C++11 or above

## Slide 35: Installing – Hardware (scanner)
Setup raspberry pi:
  https://www.raspberrypi.com/documentation/computers/getting-started.html
Connect camera to Raspberry Pi
Setup DAC0830 to create a 7.5Vmax and create a bipolar signal using unity gain and negative unity gain amplifiers
Connect bipolar signals to –X/+X and –Y/+Y for the drivers
DACs will now drive the drivers, which move the scanner

## Slide 36: Installing – Hardware (FSOC)
Plug media converters into power and plug ethernet into computers
Connect LC/UPC cables
Connect UPC side of cables to the collimator
Place lens in front of the collimator
Mirror system on receiver side

## Slide 37
GitHub

## Slide 38: Link
https://github.com/LMU-Capstone/microp

## Slide 39
Free Space Test:
Collimation

## Slide 40: Pattern Analysis – No Lens
SFP
Fiber

## Slide 41: Pattern Analysis - Lens
SFP with Lens
Fiber with Lens

## Slide 42: Divergence
Lens necessary
Fiber has minimal impact
Fiber changes scattering pattern
Setup | Divergence (mm)
SFP Only | 117.7
Fiber Only | 100.8
SFP with Lens | 5.6
Fiber with Lens | 4.8

## Slide 43
Extra Diagrams

## Slide 44: KORUZA Diagram
https://github.com/IRNAS/KORUZA/blob/master/diagrams/ElectronicsDiagram.png

## Slide 45: House of Quality

## Slide 46: SFP 1000Base-SX Specifications
Parameter | 1000Base-SX
Rate | 1000 Mbps
Optical Interface | Multimode
Maximum Distance | 62.5/125 MMF Cable 656 ft/200 m
 | 50/125 MMF Cable 1640 ft/500 m
Transmitter Wavelength | 770 through 860 nm
Average Launch Power | -9.5 through 0 dBm
Average Receive Power | -17 through 0 dBm
Receiver Saturation | 0 dBm
Receiver Sensitivity | -17 dBm
https://www.juniper.net/documentation/en_US/release-independent/junos/topics/reference/specifications/transceiver-m-mx-t-series-1000base-optical-specifications.pdf
https://www.amazon.com/10Gtek-GLC-SX-MMD-GLC-SX-MM-Transceiver-1000Base-SX/dp/B00U77VPX2/ref=sr_1_3?dchild=1&keywords=sfp%2B1000base-sx&qid=1633822790&sr=8-3&th=1

## Slide 47: KORUZA Links
Description
  https://www.hackster.io/musti/koruza-2b1824#toc-a--1-gbps-version-3
Specifications
  http://www.koruza.net/specs/
GitHub
  https://github.com/IRNAS/KORUZA

## Slide 48
Fiber Test: Throughput and Latency

## Slide 49: Fiber Testbed
Two VMs running 1 core, 2GB (3 core/4GB)
  Lower performance due to system strain but reduced overhead for experimenters
  Additional tests with more powerful machines required
Bridged to Ethernet adapter
Control was Ethernet cable only; experimental used SFP system

## Slide 50: Latency Tests
Control
Experimental (Fiber)

## Slide 51: Latency Test (combined)
Difference in speed at beginning likely a result of 'test-isms'

## Slide 52: Latency Averages
Minor differences
Much more data required to determine statistical significance
Test | Average Latency (ms)
Average Latency Control Unidirectional | 1.30
Average Latency Control Bidirectional | 1.62
Average Latency Experimental Bidirectional | 1.57
Average Latency Experimental Unidirectional | 1.57

## Slide 53: Latency Summarized
Testing Setup | Unidirectional Latency (ms)
Hardware-in-the-loop fiber | 1.32 ± 0.32
Ethernet Cable Only | 1.32 ± 0.3
Shared port | 1.06 ± 0.22
Shared network adapter | 1.1 ± 0.26

## Slide 54: Throughput Tests
Control
Experimental (Fiber)

## Slide 55: Throughput Test (combined)
Experimental closely followed control, bidirectional slows down

## Slide 56: Throughput Averages
Bidirectional slower
Unclear cause of slowdown
Control/Experimental similar
 | Experimental Average Throughput (Mbps) | Control Average Throughput (Mbps)
Average Throughput Experimental Bidirectional | 894 | 898
Average Throughput Experimental Unidirectional | 941 | 939
Average Throughput 3 Cores Experimental Bidirectional | 909 | 873
Average Throughput 3 Cores Experimental Unidirectional | 942 | 940

## Slide 57: Throughput Summarized
Testing Setup | Bidirectional Throughput (Mbps) | Parallel Bidirectional Throughput (Mbps) | Unidirectional Throughput (Mbps)
Hardware-in-the-loop fiber | 941 ± 24 | 899 ± 71 | 941 ± 22
Ethernet Cable Only | 925 ± 125 | 863 ± 112 | 941 ± 24
Shared port | 2894 ± 196 | 1633 ± 260 | 2913 ± 196
Shared network adapter | 2719 ± 334 | 1578 ± 269 | 2714 ± 427