## Slide 1
MICROP
Ian Green (& Natalia Cedeño)
Loyola Marymount University
Department of Computer Science
December 08, 2021
Notes: Marine Infrared Communication Relay with Optical Propagation (MICROP)

## Slide 2: Motivation
What is this product about && Why are we building this?
https://api.army.mil/e2/c/images/2012/11/02/270620/original.jpg
Notes: IAN
'why do you need my product'
1. this is the problem we are solving
2. why is it an important problem
-> navy AND civvy applications
-> non trival problem

## Slide 3: Solution
UAV mounted FSOC
Electro-optical transceiver
  Small form-factor pluggable (SFP) module
Near IR (850nm)
DJ Scanning Galvanometer
Static & Dynamic testing
Raspberry Pi on-board
https://www.researchgate.net/publication/338257918/figure/fig1/AS:842165353721856@1577799275060/Flying-Ad-hoc-Network-FANET.ppm
Notes: NATALIA

## Slide 4: Timeline & Scope
Previous
Design
Ordering
Static construction/testing
Spring
Scanner
Tracking
Task | Assigned To | Start | End
Research and Development |  |  | 
Static Design | Both | 9/12/21 | 9/15/21
Order parts | Ian | 9/15/21 | 10/1/21
Scanner Design | Both | 12/6/21 | 12/13/21
Tracking Algorithm | Both | 2/14/22 | 2/19/22
FANET Design | Both | 5/28/22 | 5/30/22
Static Design |  |  | 
Construct Transmitter | Ian | 10/25/21 | 12/6/21
Construct Receiver | Natalia | 10/25/21 | 12/6/21
Lab Condition Testing | Both | 12/6/21 | 12/13/21
Single Motion Design |  |  | 
Scanner Parts Ordering | Natalia | 12/13/21 | 12/18/21
Construct Scanner | Both | 1/10/22 | 1/17/22
Test Scanner | Natalia | 1/17/22 | 1/24/22
Scanner Tracking Implementation | Ian | 1/17/22 | 1/31/22
One way tracking testing | Both | 1/31/22 | 2/10/22
Dual Motion Design |  |  | 
Mount receiver on drone | Natalia | 2/10/22 | 2/17/22
Test drone receiver while moving | Natalia | 2/17/22 | 3/10/22
Mount transmitter on drone | Ian | 2/10/22 | 2/17/22
Test drone transmitter while moving | Ian | 2/17/22 | 3/10/22
Test drone-to-drone communication | Both | 3/10/22 | 4/14/22
Demonstrate FANET feasibility | Both | 4/14/22 | 4/21/22
Notes: NATALIA

## Slide 5: Challenges
Main challenges that need to be resolved in the project
Cheap free space optical
  Laser generation
  Signal Generation
    Computer limits
Scanning
  Stability
Tracking
  Moving target
  Moving own-ship
https://i.ytimg.com/vi/Y9ejz-arlAg/maxresdefault.jpg
Notes: NATALIA

## Slide 6: The Team
Ian: The CS Guy
Natalia: The EE Girl

## Slide 7: Latency Summarized

## Slide 8: Throughput Summarized

## Slide 9: Error Analysis
Testing Setup | Bidirectional Error | Parallel Bidirectional Error | Unidirectional Error
Hardware-in-the-loop fiber | 4.24E-08 | 2.18E-07 | 6.99E-08
Ethernet Cable Only | 1.08E-07 | 2.46E-07 | 7.26E-08
Shared port | 5.39E-06 | 2.78E-06 | 5.34E-06
Shared network adapter | 5.53E-06 | 2.55E-06 | 5.49E-06

## Slide 10: Demo

## Slide 11
Questions?

## Slide 12
Backup Slides

## Slide 13: Requirements
Technical Requirements
1Gbps transmit/receive
Infrared Wavelength (780nm-1mm)
20mm receiver tracking at 100m distance for maximum velocity of 100m/s
Constant updating of tracking (software)
Budget of ~$500
https://topcashbuyer.com/wp-content/uploads/500-American-Dollar-Bill-USD-with-President-William-McKinley-on-the-Face-e1574719909489.jpg
Notes: NATALIA

## Slide 14: Major Decisions
Decision matrices for most important decisions
Scanning
  Mirrors
Computer Connection
  Wire type
Laser Generation
  Wavelength
  Speed
Notes: IAN

## Slide 15: Cost
Estimated Cost
Item​ | Quantity​ | Cost​
Raspberry Pi 2B​ | 2​ | $0.00​
Raspberry Pi NoIR Camera​ | 2​ | $26.72​
850 nm Multimode Fiber SFP​ | 2​ | $26.01​
50 mm Diameter, 100 mm Focal Length Plano-Convex Lens​ | 2​ | $17.54​
Galvanometer Scanner​ | 2​ | $186.22​
Media Converter​ | 2​ | $42.54​
Visible Light Aiming Laser​ | 2​ | $39.00​
RJ45 to USB-C Converter​ | 2​ | $29.46​
CAT-8 Ethernet Cable​ | 2​ | $6.48​
50/125 Multimode LC-LC Duplex Fiber Patch Cable​ | 2​ | $18.46​
Total​ | $392.43​ | 
Notes: NATALIA
Put pictures of things that have been ordered and that we are waiting for

## Slide 16: Conclusion
Visions of the Future
Building a FSOC system using SFP modules
Testing in a dynamic system
Proof of concept for further implementation
https://spie.org/Images/Graphics/Newsroom/2020articles/B3_2_HYDRON_920.jpg
Notes: IAN

## Slide 17: Tests
Testbed information and results over time

## Slide 18: Fiber Testbed
Two VMs running 1 core, 2GB (3 core/4GB)
  Lower performance due to system strain but reduced overhead for experimenters
  Additional tests with more powerful machines required
Bridged to Ethernet adapter
Control was Ethernet cable only; experimental used SFP system

## Slide 19: Latency Test
Control
Experimental

## Slide 20: Latency Test (combined)
- Difference in speed at beginning likely a result of 'test-isms'

## Slide 21: Latency Averages
Minor differences
Much more data required to determine statistical significance
Test | Average Latency (ms)
Average Latency Control Unidirectional | 1.30
Average Latency Control Bidirectional | 1.62
Average Latency Experimental Bidirectional | 1.57
Average Latency Experimental Unidirectional | 1.57

## Slide 22: Throughput Tests
Control
Experimental

## Slide 23: Throughput Test (combined)
- Experimental closely followed control, bidirectional slows down

## Slide 24: Throughput Averages
Bidirectional slower
Unclear cause of slowdown
Control/Experimental similar
 | Experimental Average Throughput (Mbps) | Control Average Throughput (Mbps)
Average Throughput Experimental Bidirectional | 894 | 898
Average Throughput Experimental Unidirectional | 941 | 939
Average Throughput 3 Cores Experimental Bidirectional | 909 | 873
Average Throughput 3 Cores Experimental Unidirectional | 942 | 940

## Slide 25: Pattern Analysis
What does the beam look like?

## Slide 26: Pattern Analysis – No Lens
SFP
Fiber

## Slide 27: Pattern Analysis - Lens
SFP with Lens
Fiber with Lens

## Slide 28: Divergence
Lens necessary
Fiber has minimal impact
Fiber changes scattering pattern
Setup | Divergence (mm)
SFP Only | 117.7
Fiber Only | 100.8
SFP with Lens | 5.6
Fiber with Lens | 4.8

## Slide 29: Diagrams
System Diagrams

## Slide 30: KORUZA Diagram
https://github.com/IRNAS/KORUZA/blob/master/diagrams/ElectronicsDiagram.png

## Slide 31: KORUZA Links
Description
  https://www.hackster.io/musti/koruza-2b1824#toc-a--1-gbps-version-3
Specifications
  http://www.koruza.net/specs/
GitHub
  https://github.com/IRNAS/KORUZA

## Slide 32: House of Quality

## Slide 33: Spec Sheets
Product Tech Sheets

## Slide 34: SFP 1000Base-SX Specifications
Parameter | 1000Base-SX
Rate | 1000 Mbps
Optical Interface | Multimode
Maximum Distance | 62.5/125 MMF Cable 656 ft/200 m
 | 50/125 MMF Cable 1640 ft/500 m
Transmitter Wavelength | 770 through 860 nm
Average Launch Power | -9.5 through 0 dBm
Average Receive Power | -17 through 0 dBm
Receiver Saturation | 0 dBm
Receiver Sensitivity | -17 dBm
https://www.juniper.net/documentation/en_US/release-independent/junos/topics/reference/specifications/transceiver-m-mx-t-series-1000base-optical-specifications.pdf
https://www.amazon.com/10Gtek-GLC-SX-MMD-GLC-SX-MM-Transceiver-1000Base-SX/dp/B00U77VPX2/ref=sr_1_3?dchild=1&keywords=sfp%2B1000base-sx&qid=1633822790&sr=8-3&th=1

## Slide 35: Other Sheets
https://github.com/LMU-Capstone/microp/blob/baf11cad1060482e7e44d2270b1c400f65a833ad/docs/product%20sheets/LC-Product-Spec.pdf