## Slide 1
MICROP:
Project Progress Update
November 17th, 2021

## Slide 2: Reminder
Cheap, dynamic free space optical system
1Gbps
SFP Transceiver
RJ45 (Ethernet|Cat7+) connection
https://encyclopedia.pub/3726

## Slide 3: Update
Finalized design
Finalized hardware test suite
Built/used software testbed
Began free space testing

## Slide 4
Fiber Test: Throughput and Latency

## Slide 5: Fiber Testbed
Two VMs running 1 core, 2GB (3 core/4GB)
  Lower performance due to system strain but reduced overhead for experimenters
  Additional tests with more powerful machines required
Bridged to Ethernet adapter
Control was Ethernet cable only; experimental used SFP system

## Slide 6: Latency Test
Control
Experimental

## Slide 7: Latency Test (combined)
- Difference in speed at beginning likely a result of 'test-isms'

## Slide 8: Latency Averages
Minor differences
Much more data required to determine statistical significance
Test | Average Latency (ms)
Average Latency Control Unidirectional | 1.30
Average Latency Control Bidirectional | 1.62
Average Latency Experimental Bidirectional | 1.57
Average Latency Experimental Unidirectional | 1.57

## Slide 9: Throughput Tests
Control
Experimental

## Slide 10: Throughput Test (combined)
- Experimental closely followed control, bidirectional slows down

## Slide 11: Throughput Averages
Bidirectional slower
Unclear cause of slowdown
Control/Experimental similar
 | Experimental Average Throughput (Mbps) | Control Average Throughput (Mbps)
Average Throughput Experimental Bidirectional | 894 | 898
Average Throughput Experimental Unidirectional | 941 | 939
Average Throughput 3 Cores Experimental Bidirectional | 909 | 873
Average Throughput 3 Cores Experimental Unidirectional | 942 | 940

## Slide 12
Free Space Test:
Collimation

## Slide 13: Pattern Analysis – No Lens
SFP
Fiber

## Slide 14: Pattern Analysis - Lens
SFP with Lens
Fiber with Lens

## Slide 15: Divergence
Lens necessary
Fiber has minimal impact
Fiber changes scattering pattern
Setup | Divergence (mm)
SFP Only | 117.7
Fiber Only | 100.8
SFP with Lens | 5.6
Fiber with Lens | 4.8

## Slide 16: Next Steps
Construct lens holder for bi-directional testing
Increase automation of testing*
Collect more data*
*Done as of today

## Slide 17
Questions?